## Slide 1
ADVANCED MOTORSPORT SIMULATION & VEHICLE DYNAMICS
Effect of Rear-Wing Angle on F1 Car Performance
Project Scope & Methodology
• An analytical simulation of a representative Formula 1-style vehicle.
• Rear-wing sweep: 0–30° on three synthetic circuit archetypes.
• Corrected force-feasible lap solver and full-bound active-aero search.
• Verified numerical results; not CFD, measured telemetry, or a team setup.
Project Code | ME3106 Motorsport Sim
Model Version | 1.0.0
Run ID | 9b1c3a7968173ace
Angle Sweep | 0.0° to 30.0° (1° step)
Circuits | Low-DF, Balanced, High-DF
Classification | Representative Educational
Representative Educational Model · Run ID: 9b1c3a7968173ace · Seed 3106
Notes: Introduce the project as a comparative engineering experiment, not an exact F1 digital twin. The central question is whether added downforce compensates for drag over a complete lap.

## Slide 2
ME3106 · RESEARCH QUESTION
Research Question and Objectives
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 2 of 18
• How does rear-wing incidence affect aerodynamic forces and minimum lap time?
• Quantify the trade-off between straight-line resistance and cornering grip.
• Compare low-downforce, balanced, and high-downforce circuit geometries.
• Compare a fixed wing with ideal and actuator-limited two-state strategies.
Key Metrics & Specifications
Independent variable | Rear-wing angle
Main objective | Minimum feasible lap time
Secondary outputs | Speed and tractive energy
Comparison | Same car; different tracks
Notes: Explain that a wing with maximum lift-to-drag ratio is not necessarily the fastest setup. All comparisons use identical vehicle inputs and track meshes.

## Slide 3
ME3106 · ASSUMPTIONS
Study Scope and Modeling Assumptions
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 3 of 18
• Quasi-steady point-mass motion with front/rear axle load resolution.
• Analytical rear-wing polar combined with a fixed baseline full-car map.
• Load-sensitive tyres, combined grip, longitudinal load transfer, torque and gearing.
• No tyre-temperature dynamics, suspension transients, driver telemetry, or CFD.
Key Metrics & Specifications
Model scale | Full-car forces
Track spacing | No more than 5 m
Vehicle mass | 798 kg
Wheelbase | 3.60 m
Notes: State the scope before discussing results. Axle forces are resolved, but yaw handling and transient suspension behavior are not modeled. Circuit labels describe synthetic geometry, not real venues.

## Slide 4
ME3106 · AERODYNAMICS
Aerodynamic Model: Lift, Drag and Stall
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 4 of 18
• Finite-wing slope: a = a0 / [1 + a0 / (pi e AR)].
• Wing drag includes profile, induced and assumed post-stall terms.
• Pre-stall lift rises linearly; post-stall lift decays exponentially.
• The join is continuous, but its slope can kink at the assumed stall angle.
Angle bounds | 0–30°
Assumed stall | 18°
Aspect ratio | Span squared / wing area
Corrected model output; representative educational vehicle.
Notes: Explain why finite span reduces the ideal two-dimensional lift slope. The stall angle is an assumed model parameter, not an experimentally measured property of a real F1 wing.

## Slide 5
ME3106 · AERODYNAMIC FORCES
Speed-Dependent Downforce and Drag
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 5 of 18
• Dynamic pressure: q = 0.5 rho V_air squared.
• Downforce = q A CL,total; drag = q A CD,total.
• Relative air speed matters when wind is present.
• Added rear-wing force changes axle loading and the available tyre grip.
Air density | 1.225 kg/m3 nominal
Reference area | 1.50 m2
Comparison angles | 0°, 9°, 18°, 30°
Corrected model output; representative educational vehicle.
Notes: Show that force rises with air speed squared for unchanged coefficients. Distinguish the wing coefficients from the area-scaled full-car coefficients. Downforce is positive downward in this project.

## Slide 6
ME3106 · VEHICLE DYNAMICS
Tyre Grip and Longitudinal Load Transfer
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 6 of 18
• Load sensitivity: mu = mu_ref (Fz / Fz_ref)^(-n).
• Combined demand: (Fx/Fx,max)^p + (Fy/Fy,max)^p <= 1.
• Lateral demand is normalized by lateral friction, not longitudinal friction.
• Actual acceleration shifts axle normal loads and alters traction/braking capacity.
Key Metrics & Specifications
Tyre exponent n | 0.08
Ellipse exponent p | 2
Nominal mu_x / mu_y | 1.85 / 1.95
Load resolution | Front and rear axles
Notes: Describe the corrected friction-ellipse normalization. An axle already using most lateral grip cannot independently provide its full longitudinal force. Load transfer must use the achieved acceleration.

## Slide 7
ME3106 · LONGITUDINAL PERFORMANCE
Powertrain and Force Balance
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 7 of 18
• Available wheel thrust follows the interpolated engine torque curve and eight gears.
• Resistance combines aerodynamic drag, rolling resistance and track gradient.
• Each segment must satisfy thrust - brake - resistance = mass x acceleration.
• Constant-speed cornering must reserve enough longitudinal grip to overcome drag.
Key Metrics & Specifications
Gear count | 8
Driveline efficiency | 0.94
Redline | 15,000 rpm
Energy metric | Positive wheel tractive work
Notes: Explain the main physics correction: a purely lateral speed limit can permit unsustainable speed if no tyre force remains to overcome drag. The corrected solver rejects that state. No battery or hybrid deployment is modeled.

## Slide 8
ME3106 · SIMULATION METHOD
Closed-Track Lap Simulation Workflow
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 8 of 18
• Load validated car configuration and discretize the track at <=5 m.
• Construct a sustainable local speed envelope for the commanded wing profile.
• Apply forward acceleration and backward braking passes until convergence.
• Include the closing segment, then check achieved acceleration and force closure.
Key Metrics & Specifications
Speed convergence | <=0.001 m/s
Iteration ceiling | 200
Force feasibility guard | >= -5 N
Force closure guard | <=0.000001 N
Notes: Walk through the distance-domain solver. The start/finish cell is part of the physics, not a special unchecked edge. Numerical guards establish feasibility within the model, not experimental accuracy.

## Slide 9
ME3106 · CORRECTED RESULTS
Fixed-Wing Sweep Across Three Circuits
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 9 of 18
• 93 physical laps: 31 integer angles x three synthetic circuits.
• Every case checked for convergence, force feasibility and closed-segment integration.
• All angle cases retain the original 5 m track discretization.
• The best wing setting depends on this car model and the circuit geometry.
Grid cases | 93 / 93 checked
Wing sweep | 0°, 1°, ... 30°
Track types | Low-DF / Balanced / High-DF
Corrected model output; representative educational vehicle.
Notes: Use the fresh fixed-lap sweep plot, not the legacy result bundle. Discuss how curve minima differ across circuits. Do not rename the synthetic circuits as real tracks.

## Slide 10
ME3106 · FIXED OPTIMIZATION
Continuously Refined Fixed-Wing Optima
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 10 of 18
• Physical lap solves refine candidate basins around the integer sweep.
• Bounds and neighboring integer points remain part of the search.
• Balanced-track optimum is near 2.819°; the other two are near 18°.
• These are nominal model optima, not uncertainty confidence intervals.
Low-DF fixed | 17.752° / 68.927 s
Balanced fixed | 2.819° / 59.130 s
High-DF fixed | 18.000° / 64.418 s
Corrected model output; representative educational vehicle.
Notes: Report the refined optima to three decimals, then explain that more digits do not imply experimentally calibrated accuracy. The high-downforce optimum falls at the assumed stall angle.

## Slide 11
ME3106 · FIXED-WING DIAGNOSTICS
Speed and Energy: Secondary Performance Metrics
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 11 of 18
• Record maximum speed and positive tractive wheel work for every fixed lap.
• Energy is integrated from achieved tractive force over distance.
• Minimum lap time and minimum tractive energy are different objectives.
• Wheel tractive work is not fuel consumption or battery-energy demand.
Source | Fresh 93-case fixed audit
Energy unit | MJ per modeled lap
Speed unit | km/h
Corrected model output; representative educational vehicle.
Notes: Explain what the energy metric means. Avoid interpreting a tractive-work difference as a fuel-saving percentage; engine efficiency and hybrid energy flows are outside scope.

## Slide 12
ME3106 · CONTROL STRATEGY
Two-State Active Aerodynamics
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 12 of 18
• Use an open, lower-angle state on eligible straight sections.
• Use a closed, higher-angle state under the modeled switching conditions.
• Search every unique integer pair within 0–30°, with >=1° separation.
• Compare ideal state changes against finite-rate, delayed actuator behavior.
Key Metrics & Specifications
Pairs per search | 465
Actuator limit | 90°/s
Activation delay | 0.2 s
Deactivation delay | 0.1 s
Notes: The active strategy is an educational control policy, not an exact FIA implementation. The ideal mode is a model comparison; the limited mode includes actuator timing. Grid-resolved optimality is not continuous-global optimality.

## Slide 13
ME3106 · ACTIVE-AERO RESULTS
Fixed Versus Ideal and Limited Active Aero
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 13 of 18
• Compare optimized strategies using the same car and original track meshes.
• Active search evaluates actual physical laps, not a coarsened surrogate.
• All completed cases must satisfy force, convergence and actuator checks.
• Interpret small differences relative to model assumptions and numerical resolution.
Low-DF limited | 67.914 s
Balanced limited | 59.053 s
High-DF limited | 64.184 s
Corrected model output; representative educational vehicle.
Notes: Read the corrected three-strategy comparison. Report the gain in seconds from the fixed optimum to the limited strategy. These nominal gains are not guaranteed real-world performance improvements.

## Slide 14
ME3106 · NUMERICAL AUDIT
Validation and Reproducibility Evidence
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 14 of 18
• Fixed sweep: 93 checked laps, including force, time and energy closure.
• Active searches: 465 unique pairs per circuit and actuator mode.
• Scalar force checks include the track closing segment and achieved acceleration.
• Source hashes, input hashes, runtime versions and completion receipts preserve identity.
Key Metrics & Specifications
Active scope | 3 circuits x 2 modes
Active cases | 2,790 total
Audit type | Numerical feasibility
Empirical validation | Not performed
Notes: Distinguish the six active grids: the balanced ideal grid completed earlier, while the five monitored grids contribute 2,325 cases. Passing these guards does not make the whole software suite or native implementation complete.

## Slide 15
ME3106 · NATIVE TOOLCHAIN
MATLAB and Simulink Implementation
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 15 of 18
• MATLAB source includes configuration, aero, dynamics and fixed-wing lap analysis.
• Simulink model/builder is supplied for a speed-dependent aero/actuator demonstration.
• The aero block chain is: speed and angle -> coefficients -> forces -> scopes.
• Full native active/uncertainty/sensitivity execution and strict runtime parity remain unverified.
Key Metrics & Specifications
MATLAB entry point | matlab/run_project.m
Parity tolerance | 1e-4 required
Simulink scope | Aero/actuator demonstration
Runtime status | Full native validation pending
Notes: Show the actual source/model files if demonstrating the project. Do not say all results were produced by MATLAB: the corrected numerical evidence here comes from Python. MATLAB startup failed in this environment, and full native scope is incomplete.

## Slide 16
ME3106 · RESEARCH LIMITATIONS
Uncertainty and Sensitivity: What Remains
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 16 of 18
• A validated >=1,000-sample, nine-parameter uncertainty study is still required.
• The tested uncertainty surrogate failed independent validation and was rejected.
• Direct full-physics Monte Carlo is selected, but not yet implemented or executed.
• No confidence intervals or sensitivity rankings are claimed in this presentation.
Key Metrics & Specifications
Planned random seed | 3106
Planned samples | >=1,000 per circuit
Accepted uncertainty | None yet
Legacy MC figures | Excluded
Notes: Be direct: uncertainty results are unfinished. Explain the planned sample-angle physical simulations, but do not present the proposal as completed work. This transparency is stronger than displaying invalid confidence intervals.

## Slide 17
ME3106 · CONCLUSIONS
Main Findings and Engineering Interpretation
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 17 of 18
• There is no universal wing angle: optimize for the complete circuit, not one aerodynamic metric.
• Correct force balance changes the accepted lap speeds, optima and strategy comparisons.
• Two-state active aero provides a nominal model benefit when feasible switching is allowed.
• Final empirical calibration, native parity and validated uncertainty are necessary next steps.
Key Metrics & Specifications
Nominal fixed optimum | Circuit dependent
Control takeaway | Respect actuator limits
Model takeaway | Reserve grip for resistance
Claim boundary | Educational simulation
Notes: Conclude with the engineering trade-off and the corrected feasibility requirement. Explain that the deliverable is a defensible presentation of verified nominal results, not a declaration that every original project requirement is satisfied.

## Slide 18
ME3106 · REFERENCES & HANDOFF
Evidence, Source Files and Questions
Representative Educational Model · Run ID: 9b1c3a7968173ace · Slide 18 of 18
• Inputs: config/project.json and tracks/*.json define assumptions and geometry.
• Physics: src/f1wing/aero.py, dynamics.py, lap.py and strategies.py.
• Corrected results: docs/verification/*-20261005.csv and matching JSON audit receipts.
• Native files: matlab/ and results/simulink/; incomplete runtime scope is disclosed.
Key Metrics & Specifications
Presentation | Editable PowerPoint + PDF
Speaker support | Notes and slide-by-slide guide
Numerical source | Corrected audit receipts
Questions | Model, methods, trade-offs
Notes: Invite questions about the equations, numerical guards, optimization and limits. If asked about a real F1 setup or robust optimum, say that calibrated aerodynamic/tyre data and validated uncertainty are still needed.